Translation Matrix

T =

Rotation Matrix

R =

Combine to get the Transformation Matrix

T = T ◦ R =

=

For a robotic arm of 2 links rotating in R2

Give each link its own coordinate system

θ is the angle between the coordinate systems

Transformation Matrix

T2 =

Places the vector v2 in the frame A1 of v1

Transformation Matrix

T1 =

Places the vector v2 in the general frame A (x,y)

Combine the Transformations

T1◦T2 =

Where a = 1 and b = 0

T1◦T2 =

=

Multiply the Transformations by the initial vector v1

T1◦T2◦v1 =

=                                           =

Which gives the final location of the arm

(1)	cos(θ1+θ2) + cosθ1 = x

(2)	sin(θ1+θ2) + sinθ1 = y

Solve (1) for (θ1+θ2)

θ1+θ2 = cos-1(x-cosθ1)

Solve (2) for (θ1+θ2)

θ1+θ2 = sin-1(y-sinθ1)

Substitute

cos-1(x-cosθ1) = sin-1(y-sinθ1)

sin(cos-1(x-cosθ1)) = sin(sin-1(y-sinθ1))

y-sinθ1 = sqrt(1-( x-cosθ1)2)

Square the equation

(y-sinθ1)2 = 1-( x-cosθ1)2

y2-2y sinθ1+ sin2θ1 = 1-x2+2xcosθ1-cos2θ1

cos2θ1+sin2θ1 = 1

x2+y2 = 2xcosθ1+2y sinθ1

x2+y2 = r2

xcosθ1+ysinθ1 = r2/2

acosθ+bsinθ = sqrt(a2+b2)sin(θ+tan(b/a))

sqrt(x2+y2)sin(θ1+tan-1(y/x)) = r2/2

sin(θ1+tan-1(y/x)) = r/2

θ1+tan-1(y/x) = sin-1(r/2)

θ1 = sin-1(r/2)-tan-1(y/x)

Substitute back into (2)

sin-1(r/2)-tan-1(y/x)+θ2 = sin-1(y-sin(sin-1(r/2)-tan-1(y/x)))

θ2 = sin-1(y-sin(sin-1(r/2)-tan-1(y/x)))-sin-1(r/2)+tan-1(y/x)

Thus

θ1 = sin-1(r/2)-tan-1(y/x)

θ2 = sin-1(y-sin(sin-1(r/2)-tan-1(y/x)))-sin-1(r/2)+tan-1(y/x)

Example

x = (1+sqrt(3))/2

y = (1+sqrt(3))/2

θ1 = sin-1(r/2)-tan-1(y/x)

θ1 = sin-1(sqrt(x2+y2)/2)-tan-1(y/x)

θ1 = sin-1(sqrt(2+sqrt(3))/2)-tan-1(1)

θ1 = sin-1(0.9659)-tan-1(1) = 30◦

θ2 = sin-1(y-sin(sin-1(r/2)-tan-1(y/x)))-sin-1(r/2)+tan-1(y/x)

θ2 = sin-1(y-sin(30◦)-30◦

θ2 = sin-1((1+sqrt(3))/2-sin(30◦)-30◦

θ2 = sin-1(sqrt(3)/2)-30◦

θ2 = 30◦

# Text boxes

[

]

1	0	a

0	1	b

0	0	1

[

cosθ	-sinθ	0

sinθ	cosθ	0

0	0	1

]

1	0	a

0	1	b

0	0	1

]

[

]

cosθ	-sinθ	0

sinθ	cosθ	0

0	0	1

[

]

[

cosθ	-sinθ	a

sinθ	cosθ	b

0	0	1

V2

V1

θ1

θ2

x2

y2

x1

y1

cosθ2	-sinθ2	a

sinθ2	cosθ2	b

0	0	1

]

[

x

y

(x,y)

(x,y)

y

x

V

y1

x1

θ1

cosθ1	-sinθ1	0

sinθ1	cosθ1	0

0	0	1

]

[

cosθ1	-sinθ1	0

sinθ1	cosθ1	0

0	0	1

]

[

cosθ2	-sinθ2	1

sinθ2	cosθ2	0

0	0	1

]

[

[

cosθ1cosθ2-sinθ1sinθ2	  -cosθ1sinθ2-sinθ1cosθ2   cosθ1

sinθ1cosθ2+cosθ1sinθ2	  -sinθ1sinθ2+ cosθ1cosθ2  sinθ1

0			  0			     1

]

[

]

cos(θ1+θ2)	-sin(θ1+θ2)	cosθ1

sin(θ1+θ2)	 -cos(θ1+θ2)	sinθ1

0		 0		1

]

cos(θ1+θ2)	-sin(θ1+θ2)	cosθ1

sin(θ1+θ2)	 -cos(θ1+θ2)	sinθ1

0		 0		1

[

]

[

1

0

1

]

cos(θ1+θ2) + cosθ1

sin(θ1+θ2) + sinθ1

1

[

x

y

1

]

[

30◦

30◦

((1+sqrt(3))/2, (1+sqrt(3))/2)